## Slide 1: Water cooling

## Slide 2
20240713_161526
20240713_161526
20240714_152102

## Slide 3
WATER COOLED OPTION
Cooling:
Standard version: forced air (internal fans).
Optional: water-cooled heat sinks Coolant inlet and outlet fittings: 1/8 in. female BSPT
Operating Temperature:
+5 to +40 °C (41 to 104 °F) on standard models and configurations.
With water-cooled option: +5 to +50 °C (41 to 122 °F).
19:58 pm 7/13/2024
Rm 1039

## Slide 4
The water cooled option has two major advantages. The coldhead can now be used in ambient temperatures up to +50 °C and the heat (±100 W in nominal operation) can be dissipated away from the detector system. For the power controller the maximum operating temperature still is limited to +40 °C.
The water cooled coldhead is fitted with 2x male 3/8 in. BSP threaded fittings for the inlet and outlet of the coolant.
A closed loop chiller and external coolant flow lines need to be provided separately. The type of chiller and external flow lines depend on each specific installation.